## Slide 1: Guiding Dynamic Motion Planning with Low-Dimensional PRM
Thorn Prescott & Shyam Rajendren
Le, D., & Plaku, E. (2014, September). Guiding sampling-based tree search for motion planning with dynamics via probabilistic roadmap abstractions. In 2014 IEEE/RSJ International Conference on Intelligent Robots and Systems (pp. 212-217). IEEE

## Slide 2: Introduction
Robot Dynamics constrain motion
Dynamics Equations
  High Dimensional
  Nonlinear
Solutions
  Workspace Decomposition
  Sample-Based Planning
Paper uses PRM on Simplified Environment

## Slide 3: Method Overview
Highlighted:
  Roadmap Abstraction
  Heuristic Costs
  Guiding Expansion
C: Simplified Configuration Space
S: Actual Configuration Space

## Slide 4: Roadmap Abstraction
Configuration Space C
  Low-Dimensional
  Related to S
Construct Roadmap in C with PRM
  Sampling to create Vertices and Edges
  Nearest Neighbors and Distance Metric
  Additional Sampling as needed

## Slide 5: Heuristic Cost Generation
Heuristic Used
  Shortest Path from Goal to ()
  Dijkstra’s Starting at Goal

## Slide 6: Guiding Expansion
Tree built starting at
function S → C
  Each is in a group based on nearest
Iteration
  Select a Group
  Create Trajectory to point in Group

## Slide 7: Guiding Expansion: Selecting Tree Group
Weight given to group
  Heuristic
  Frequency Group has been Selected
Maximum weighted group selected

## Slide 8: Guiding Expansion: Expanding Tree Group
Sample Target Configuration
  0.85 Near Roadmap
  0.15 From entire C
Select closest to Target from Group
Trajectory to made via control inputs
  Stop at Collision or step limit
  Points along Trajectory added to Tree

## Slide 9: Experiments and Results
Experiments were done using three models
  Physics-based vehicle model
  High-dimensional snake-like model
  Aerial-vehicle model

## Slide 10
Physics-based vehicle model
High-dimensional snake-like model
Aerial-vehicle model

## Slide 11
Color represents distance from goal. Blue means you are far away from the goal. Red means you are closer to the goal.

## Slide 12: Roadmap Abstractions used in the Experiments
The number of initial samples is set to n = 10000 and the number of neighbors is set to k = 10
An additional 5000 samples are added to the roadmap if the initial roadmap configuration does not find a path between start and goal

## Slide 13: Methods used in the Comparisons
The approach used while using roadmaps is referred to as P[prm]
The approach used while using workspace decompositions is referred to as P[ws]
The methods used for comparison are RRT, fRRT, PDST, IST, KPIECE

## Slide 14: Problem Instances
Each model was tested on sixty different runs
The best five and worst five runs are removed from the result average
For the vehicle model, runs are produced by putting the car and goal at random positions
For the other two models, the robot is placed at one end of the scene while the goal is placed at random at the other end of the scene
Run time is the time between accepting an input to when a solution is found
Results are provided along with their standard deviation

## Slide 15: Results

## Slide 16: Results
Results when varying the number of roadmap configurations and nearest neighbors

## Slide 17: Reasons for Improvement
The roadmap abstractions more effectively guide the motion-tree expansions as the roadmap uses a geometric shape that more closely relates to the full robot model as opposed to just using a point
The roadmap samples and edge connections help identify collision-free regions from which the tree search can be expanded
As a result, the roadmap abstractions provide the planner with more reliable suggestions of how to effectively reach the goal

## Slide 18: Conclusion
Experimental results show that the proposed algorithm is significantly faster than existing popular algorithms
Results show a significant speedup when using roadmap abstractions when compared to using workspace decompositions